## Slide 1: DRD Solar Home Systems in Myanmar: Findings from Nov / Dec 2014 field visit
NEP Workshop on Off-Grid Electrification in Myanmar
Grand Ball Room, Thingaha Hotel, Nay Pyi Taw
January 28-29, 2015
Chris Greacen
Notes: Honorable deputy minister, distinguished guests, renewable energy experts – it is an honor to be here.
As part of the World Bank’s efforts to assist with Myanmar’s offgrid electricity access work, it was important to develop a clearer understanding of what was happening in the field with solar electricity, particularly systems installed under the DRD’s offgrid program. I will present the result of three weeks of field work. Tomorrow I will give another presentation that will help inform a discussion of recommendations and next steps.
I would like to point out upfront that I will point out some areas where the performance of solar home systems installed under the DRD program is less than perfect. This is not meant to be a criticism of DRD. The DRD has accomplished a very impressive amount under difficult circumstances, getting tens of thousands of solar home systems installed in remote homes at relatively low cost. I have been moved both by DRD’s hard work ethic. I have also been impressed by the organization’s openness to discussing challenges and how to address them. In this spirit of speaking frankly about challenges and how to address them, I present these findings.

## Slide 2: Outline
Scope of survey
Background
Benefits of SHS
Usage patterns
Key problems
  Wiring
  Solar panel
  Controller & inverter
  Battery
  Lighting
Company profiles
SHS equipment solar in rural market towns
Notes: My talk today draws from a report to the World Bank that will be circulated soon, entitled DRD Solar Home Systems (SHS) in Myanmar: Status and Recommendations. The report is available in hard copy (state where) and is also available on the web at tiny.cc/DRDSHS2015
I will briefly discuss the scope of the survey, provide a little bit of background information of the DRD SHS program, discuss clear evidence of benefits of SHS reported by users in Myanmar, and usage patterns. I will then turn to key problems observed, including wiring, solar panel, controller, and battery. We wil look briefly at the profiles of some companies participating in the DRD SHS tender program, and finally end with a glimpse of SHS equipment that appears to be widely available in rural market towns.

## Slide 3: Scope & Methodology
Village visits
  Kayin State, Thanintharyi District, Shan State
  In-depth interviews with 26 households in 10 villages with DRD SHS
    1288 total households
    597 households receiving SHS (+27 schools, etc.)
6 DRD offices
SHS companies
  5 in Yangon, 1 in Hpa An
ITC companies
  1 cell phone company, 2 tower companies

## Slide 4: Background
FY 2013-14
  DRD solar home systems (SHS) installed in approximately 300 villages
  4 billion kyat government budget
FY 2014-15
  Over 170,000 new SHS in 1491 villages
  37 billion kyat budget
SHS procured through tender process
Given to users (100% subsidy)

## Slide 5: Specifications
Notes: This is the specification for SHS to be installed in this FY, as provided by the NPT DRD office. The specification closely matches the SHS – mostly installed last FY – that I observed in the field.
Specifications include an 80 watt solar panel, 65 Ah 12-volt battery, a controller, a 300 watt inverter, two small LED lights and one larger one; and a phone charger. The main components have a warranty of 5 years, with 1 to 2 years for the battery. The total cost per system, installed, has a recommended price cap of 200,000 kyat – a remarkably low price.
What the specifications don’t say is as important as what they do say. There is no listing of specific quality standards with which equipment must comply. There is no

## Slide 6: Village selection
Township
Develops village list
District
Aggregate & refine
State
Aggregate & refine
NPT
Aggregate, finalize
State
Adjusts according to actual budget
District
Initiates tendering process
Time
Parliament approves budget
Village
Allocates SHS to households
Tendering Process
Level

## Slide 7: Benefits of SHS
Before SHS
  2600 to 50,000 Kyat/month (average 13,400 K/month)
  Candles and kerosene/diesel
After SHS
  Mostly 0 Kyat/month (except candle for altar)
Chart: KYAT PER MONTH
Before SHS | 50000 | 45000 | 30000 | 20000 | 20000 | 16000 | 12000 | 10000 | 10000 | 7500 | 7000 | 6500 | 6000 | 6000 | 5250 | 4500 | 4000 | 3500 | 3000 | 2600
After SHS | 15000 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 7000 | 6500 | 0 | 0 | 0 | 0 | 0 | 0 | 3000 | 0
Reduced energy expenditures

## Slide 8: Usage patterns
Lights
  3 to 10 hours / night (average 4.9)
TV
  Used in 47% of households surveyed
    4 used 12-volt DC TVs, rest used inverter
  TV watching often not possible in rainy season
Cell phone charging

## Slide 9: Key problems – wiring
Wiring
  Poorly secured interior wiring (all SHS investigated)
  Poor splices PV-to-controller wire (90%)
  No UV resistant insulation on PV-to-controller wire (>90%)
  poor splices: wires simply wrapped and taped, very exposed to rain
  Indoor-rated wire has no UV protection

## Slide 10: Key problems – solar panel
Underperforming
  >80% perform below 50% of Isc spec*.
Not facing south
  77% exceeded 15° deviation from true south
Some poorly mounted
  >10% on weak rot-prone wooden poles
Significant shading
  >15% of panels have shading problems (5 meters cable is too short)
  * temperature, insolation-compensated

## Slide 11: Key problems – controller & inverter
Controller
  Bypassed in 17% of SHS inspected
  Failure in 20% of SHS inspected
Inverter
  Failure in 17% of SHS inspected
  Village leader estimates:
    Taung Pa Le village (Thanintharyi State) about 60 households used the inverter to power a TV. Of these 60 households, the inverters in 90% have failed.
    Ma Saw Pyin Gyee (Thanintharyi State) 50% of inverters failed.

## Slide 12: Key problems – battery
Battery failures in 3 out of 24 SHS inspected, however…
  … visiting mostly during day meant that some batteries looked OK that actually were probably not healthy
(Many) more failures expected within this year as batteries age
Battery voltage 8.0 volts
Plates exposed from overcharging

## Slide 13: Key problems – lighting
LED bulb/fixture failures
  … in 17% of SHS inspected
Inverters were used to power lights…
  … in systems installed by 3 out of 12 companies
  (not recommended – less efficient and leaves home without lights if inverter fails)
Interior lamp fixtures used in outdoor applications with insufficient rain protection

## Slide 14: Six companies participating in DRD SHS program
Name of Company | Type of product/ service offered | Number of staff | solar sector experience | SHS built to date | Sourcing of components for DRD SHS | Revenues (Thousand US$/year) | Expected increase FY2014-5
Moe Ko San Solar | SHS and mini-grids | 33 | 2 years | 780 | Korea, China | 160 | 200%
T & t Co. Ltd | SHS and mini-grids. Solar street lamps | 20 | 1.75 years | 2722 | China | 80 | 1000%
Asia Solar | From pico-solar products to projects > 10 kW | 170 | 5 years | 7822 | China | >1,000 | >200%
Earth Renewable Energy Company | SHS, 1-3 kW systems | 25 | 12 years | 3700 | China | 1,000 | 40%
Myanmar Mahar Htun | SHS | 6 involved in PV. (60 total) | None | 0 | China | 233 | N/A
SolaRiseSys | PV for telecom, SHS, mini-grids, lanterns | 50 | 4 years | 10208 | China | not divulge | not divulge

## Slide 15: SHS company challenges
Wide variety of experience levels (0 to 12 years)
For all:
  Difficult to stay in business at 200,000 kyat/SHS
  Difficult to honor warranty considering transaction costs to rural sites
  Cashflow challenges -- interested in trade finance

## Slide 16: Solar equipment widely sold in shops in rural market towns
Questionable quality Inexpensive
Item | Brand | Country | Size | Price (Kyat)
PV panel | Tata | India | 20 watt | 18,000
PV panel | Tata | India | 38 watt | 30,000
PV panel | Tata | India | 80 watt | 60,000
LED TV/DVD | Sanook | Thailand | 11.6" | 43,000
Inverter | No brand | China | 350 watt | 18,000
Battery | 3K | Thailand | 2, 4…12 V | 33,000

## Slide 17: User-purchased SHS
Very common
  Installed in >25% of households along main rural roads in areas visited
  In homes visited with DRD SHS, 25% also had user-purchased SHS
Similar problems as DRD SHS…
  Improper mounting, orientation of PV
  Wire with no UV protection
  Poor household wiring
  Failed batteries
… but generally worse
  Usually no charge controller
  Voltage mismatch issue

## Slide 18: Hire-purchase SHS
Who: Mandalay State Project Planning Dept + Heatec
How many: “Thousands” installed in Mandalay
Specifications: 40 watt PV, 40 Ah battery
Price: 450,000 kyat to be paid back in 1 year, 9.75% interest
Equipment quality: Similar to DRD SHS.

## Slide 19: Solar PV and ICT
    Solar hybrid systems to power towers
    Cell phone towers as anchor customers
    Solar PV for charging cell phones
    Cell phone network transmit mini-grid performance data
    Electricity purchases via “Mobile money”

## Slide 20: Summary
SHS very useful for villagers
Significant technical problems in:
  Wiring
  Solar panel
  Controller & inverter
  Battery
Companies participating in tender have challenges:
  Wide differences in experience
  Challenges with cash flow
SHS equipment widely sold in rural market towns
  Inexpensive but questionable quality

## Slide 21: Thank you!
Chris Greacen
chrisgreacen@gmail.com